## Slide 1: First Dual Cross Country

## Slide 2: Lessons leading up to XC
Stage I, Lesson 4
  Safety of flight, Airports, Aeronautical charts, Airspace
Stage I Lesson 5
  RADAR and ATC, Radio Procedures, Sources of Flight Info
Stage II, Lesson 9
  Weather Forecasting Process, Printed Reports and Forecasts, Graphic Weather Products, Sources of Weather Info
Stage III, Lesson 11
  Predicting Performance, Weight and Balance, Flight Computers
Stage III, Lesson 12
  Pilotage and Dead Reckoning, VOR Navigation, ADF Navigation, Advanced Navigation (VORDME/GPS/INS)
NOW we plan a dual cross country flight!

## Slide 3: Review – Questions?
The Forecasting Process
  Forecasting methods
  Types of forecasts
  Compiling and processing weather data
  Forecasting accuracy and limitations
Notes: Jeppesen Syllabus – Stage II Ground Lesson 09

## Slide 4: Review – Questions?
Printed Reports and Forecasts
  Aviation Routine Weather Report (METAR)
  Radar Weather Reports
  Pilot Weather Reports
  Terminal Aerodrome Forecasts (TAF)
  Aviation Area Forecast (FA)
  Winds and Temperature Aloft Forecasts
  Severe Weather Reports and Forecasts
  AIRMET/SIGMET/Convective SIGMET
Notes: Jeppesen Syllabus – Stage II Ground Lesson 09

## Slide 5: Review – Questions?
Graphic Weather Products
  Surface analysis chart
  Weather Depiction Chart
  Radar Summary Chart
  Satellite Weather Pictures
  Low-level Significant Weather Prog Charts
  Convective Outlook Chart
  Forecast Winds and Temperatures Aloft Chart
  Volcanic Ash Forecast and Dispersion Chart
Notes: Jeppesen Syllabus – Stage II Ground Lesson 09

## Slide 6: Review – Questions?
Source of Weather Information
  Pre-flight weather sources
  In-flight weather sources
  Enroute Flight Advisory Service
  Weather Radar Services
  Automated Weather Reporting Systems
Notes: Jeppesen Syllabus – Stage II Ground Lesson 09
Notes:
EFAS Update: https://en.wikipedia.org/wiki/Flight_watch
EFAS now 122.2 – no more 122.0
Also FIS-B via ADS-B IN

## Slide 7: Review…questions?
Predicting Performance
  Aircraft Performance and Design
  Chart Presentations (Sectional, TAC etc.)
  Factors affecting performance
  Takeoff and Landing performance
  Climb Performance
  Cruise Performance
  Using Performance Charts
Notes: Jeppesen Syllabus – Stage III Ground Lesson 11

## Slide 8: Review…questions?
Weight and Balance
  Importance of Weight
  Importance of Balance
  Terminology
  Principles of Weight and Balance
  Computation Method
  Table Method
  Graph Method
  Weight shift formula
  Effects of operating at High Total Weights
  Flight at various CG positions
Notes: Jeppesen Syllabus – Stage III Ground Lesson 11

## Slide 9: Review…questions?
Flight Computers
  Mechanical Flight Computers
  Time, speed and distance
  Airspeed and Density Altitude Computations
  Wind Problems
  Conversions
  Solving multi-part problems
Notes: Jeppesen Syllabus – Stage III Ground Lesson 11

## Slide 10: Review…questions?
Pilotage and Dead Reckoning
  Pilotage,
  Dead Reckoning
  Flight Planning
  VFR Cruising Altitudes
  Flight Plan
  Lost Procedures
Notes: Jeppesen Syllabus – Stage III Ground Lesson 12

## Slide 11: Review…questions?
VOR Navigation
  Ground and Airborne equipment
  VOR Orientation and Navigation
  VOR Checkpoints and Test signals
  VOR Precautions
  HIS
  DME
Notes: Jeppesen Syllabus – Stage III Ground Lesson 12

## Slide 12: Review…questions?
ADF Navigation
  ADF Equipment
  Orientation
  Homing
  ADF Intercepts and Tracking
  Movable Card Indicator
  RMI (Radio Magnetic Indicator)
  ADF Limitations
Notes: Jeppesen Syllabus – Stage III Ground Lesson 12

## Slide 13: Review…questions?
Advanced Navigation
  VOR/DME based navigation
  INS
  GPS
Notes: Jeppesen Syllabus – Stage III Ground Lesson 12

## Slide 14: Cross Country Planning
The flight planning process
  Flight Overview
  Developing a route
  Preflight weather briefing
  Completing a Navigation Log
  Flight Plan – creating and filing
  Preflight inspection
Notes: Stage III, Lesson 14

## Slide 15: Cross Country Planning
The Flight
  Departure – KCRQ
  Destination – KCNO (Chino)
  Diversion airport
  Return to KCRQ
  Two souls; Student and CFI both in front seat (JD is 145 lbs.)
  Full fuel
Notes: Stage III, Lesson 14

## Slide 16: Cross Country Planning
The Regs – what do we need?
  Called out in CFR 14, Part 91, 91.103 (preflight action)
    Weather reports and forecasts (WX-Brief/DUATS/Foreflight, etc.)
    Fuel requirements for the flight
    Alternatives if the flight cannot be completed (diversion)
    Runway lengths at airport of intended use (ANY flight - Chart Supplement, Sectional)
    Takeoff and Landing performance data (POH/AFM)
  Fuel requirements. VFR day requirements (91.151)
    First airport, alternate then 30 minutes at normal cruise
      Night – 45 mins

## Slide 17: What do we need?
Sectional Chart
Chart Supplement
Flight Computer (E6B)
Plotter
Weight and Balance information for our airplane
Flight Performance for our airplane
A Navigation Log (Jeppesen in this case)
Notes: Stage III, Lesson 14

## Slide 18: Where are we going? Which Route?
Pick a destination – KORS?
Put first entry in NavLog – KPAE
Next enter Top Of Climb (TOC)
Enter additional waypoints
Enter Top Of Descent (TOD)
Enter final destination
Pick Altitude based on VFR Flight Rules
Notes: Above 3k, East=odd plus 500. West=even plus 500 feet
MAGNETIC

## Slide 19: Determine True Course, Wind and TOC
Draw lines between checkpoints on sectional
Get Winds and rule of thumb temperature and winds aloft
Using POH, determine TAS and distance to TOC
  Plus taxi, takeoff and fuel burned to TOC
  Add to Nav Log

## Slide 20: Determine Cruise and TOD
Determine cruise speed and fuel burn based on power settings and altitude
Determine at cruise distance covered to lose altitude from TOD to TPA

## Slide 21: Distances and Winds, ETE and Fuel
Using plotter, get leg distances
  Ensure SECTIONAL and NAUTICAL
Using Winds Aloft, determine WCA +/- and Groundspeed
  Winds are TRUE unless spoken
TC +/- WCA = TH +/- Var = MC +/- Dev = MH
We have distance and speed (GS) so we can calculate time (ETE)
  Use E6B
Calc Fuel totals, Total distance and total ETE (for flight plan and reserves)
Notes: The general rule is:
If you read it, it's true. If you hear it, it's magnetic.
All charts and textual sources (METAR, TAF, winds aloft, surface analysis charts, etc) use true north as the reference.
ATIS/AWOS/ASOS broadcasts, or any information a controller gives you over the radio, is magnetic.
Wind direction broadcast over FAA radios is in reference to magnetic north.
AIM Section 7-1-11 (page 7-1-26 in the 5/26/16 edition)
One exception to the "if you hear it" rule is that a FSS briefer will read you the winds referenced to true north, since they're just reading you the charts/textual information.

## Slide 22: Final preparation
Perform Weight and balance
  People, Fuel, Bags and reserve
Runway lengths for takeoff and landing airport
  POH often has takeoff and landing at gross weight for rule of thumb
Call/Connect to FSS and ensure a full weather briefing and FILE A FLIGHT PLAN
LAST CALL FOR GO/NO-GO!

## Slide 23: Appendix

## Slide 31
Notes: True Course 318 degrees true
54 nm
Gallons used 172M 3.8g
00:31 flight time